## Slide 1
MODFLOW & More
2019
The LNF Model for MODFLOW 6
Sorab Panday, Christian D. Langevin, Joseph D. Hughes, Richard G. Niswonger, and Alden Provost

## Slide 2
Presentation Outline
The MODFLOW 6 framework
The LNF Model
The Exchanges – LNF-LNF & GWF-LNF
Implementation
Applications Example

## Slide 3
The MODFLOW 6 framework

## Slide 4: Drivers
MODFLOW is not just for groundwater anymore
  Processes abound – CFP, MNW, SWR, SFR, UZF, OBS – need unified framework
  To provide a plug-and-play capability for linking or coupling new or existing models of various processes, formulations, and scales to MODFLOW and to each other
  Provide a unified solution framework for holistic water modeling
Complexity of models
  Help simplify inputs, outputs and analyses by making separate models of the complex intersections of otherwise simpler models
  For example, LGRs (and sub-layering) can be separate models, differently nested layers can be separate models
  Keeping different process models and input/output files independent
  Simplify post-processing for calibration or documentation
Modernize
  Upgrade program design and steady-state/transient input/output
  Discard outdated functionality
  Consolidate boundaries and increase flexibility

## Slide 5: Framework salient features
Plug-and-play capability for different models
  Different models can be integrated simply by supplying the appropriate local-level matrix for each model well as the appropriate exchange terms, to the object-oriented framework
Different models, model formulations, or linearization schemes can integrate and operate within a single cohesive modeling environment
  Entire matrix of flow equations for all models and exchanges solved simultaneously
  Each model solved separately with iteration on the exchange terms

## Slide 6
The LNF Model

## Slide 7: LNF model salient features
Flow through network of one-dimensional features
  Horizontal; vertical; angled
Flow formulations
  Laminar
  Hazen-Williams
  Manning
  Darcy-Weisbach
Solution Options
  Saturated or Unconfined
  Flow to Dry Cell
  Picard or Newton linearization
Section Geometries
  Circular
  Rectangular
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 8
The Exchanges – LNF-LNF & GWF-LNF

## Slide 9: GWF-LNF Exchange salient features
Exchange of flux between cells of different models
Exchange formulations
  Leakance
  Flow across skin of specified hydraulic conductivity and thickness
  Modified Thiem solution to include skin resistance/well efficiency
Solution Options
  Saturated or Unconfined
  Flow to Dry Cell
  Picard or Newton linearization

## Slide 10
Implementation

## Slide 11
Coding Narrative
LNF is a new model
  MODFLOW 6 formulation flow features/options adopted
  MODFLOW 6 input/output structure adopted
  Coding was at the local (LNF model) level for cell numbering and matrix assembly (framework puts it all together)
Needed to extend the numerical model base type
  Adds new model into framework
  Methods/subroutines of new model called in correct places
Slight learning curve for object-oriented Fortran
Some debugger obstacles, but…
Efforts were mostly to develop and debug the new LNF model with little effort required to drop it in to the framework

## Slide 12
Application Example

## Slide 13
3 Models: Gwf1; Gwf2; Lnf1
Lnf1
Gwf2
Gwf1
h = 0
h = 1
First example problem from MODFLOW-USG document
  0 to -100 m depth
  K = 1 m/d
  BUT with semi-circular canal as shown
  Gwf1: 7x7; 100 m side
  Gwf2: 9x9; 33.3 m side
  Lnf1: 4 cells
    1 = 50 m long
    2, 3, 4 = 100 m long

## Slide 14
BEGIN OPTIONS
END OPTIONS
BEGIN TIMING
TDIS simulation.tdis
END TIMING
BEGIN MODELS
#modeltype namefile modelname
GWF model1.nam GWF_Model_1
GWF model2.nam GWF_Model_2
LNF model3.nam LNF_Model_1
END MODELS
BEGIN EXCHANGES
GWF-GWF gwf1-gwf2.exg GWF_Model_1 GWF_Model_2
GWF-LNF gwf1-lnf1.exg GWF_Model_1 LNF_Model_1
GWF-LNF gwf2-lnf1.exg GWF_Model_2 LNF_Model_1
END EXCHANGES
BEGIN SOLUTION_GROUP 1
#implicit exchange
MXITER 1
NUMERICAL simulation.ims GWF_Model_1 GWF_Model_2 LNF_Model_1
#
#explicit exchange
#MXITER 10
#NUMERICAL simulation.ims GWF_Model_1
#NUMERICAL simulation.ims GWF_Model_2
#NUMERICAL simulation.ims LNF_Model_1
END SOLUTION_GROUP
Integrating the models: mf6.nam
Define all Models
Define all Exchanges
Define Solution

## Slide 15
LNF Model: NAME File
Open Input Files
Open Output Files
BEGIN OPTIONS
END OPTIONS
BEGIN INPUT_FILES
DIS8 model3.dis
GEO8 model3.geo
IC8 model3.ic
NPF8 model3.npf
OC8 model3.oc
STO8 model3.sto
data model3.disu.dat
END INPUT_FILES
BEGIN OUTPUT_FILES
LIST model3.list
DATA(BINARY) model3.hds
DATA(BINARY) model3.ddn
DATA(BINARY) model3.cbc
END OUTPUT_FILES

## Slide 16
# Unstructured discretization file
begin options
LENGTH_UNITS meters
end options
begin dimensions
nodes 4
nja 10
end dimensions
begin disdata
fleng
internal 1.0 (free) 1 fleng
50.0 100.0 100.0 100.0
felev
constant -10.0
fangle
constant 0.0000
end disdata
begin connectiondata
iac
external 'model3.disu.dat' 1 (free)
ja
external 'model3.disu.dat' 1 (free)
end connectiondata
LNF Discretization File
Options
Discretization Data
Define Connectivity
Dimensions
2 3 3 2
1 2
2 1 3
3 2 4
4 3

## Slide 17
LNF Model: Geometry File
List Sections
BEGIN OPTIONS
PRINT_INPUT
END OPTIONS
BEGIN DIMENSIONS
GEOMETRY_LIST 1
END DIMENSIONS
BEGIN GEOMETRY_LIST
CIRCULAR 1 NAME 'semi-circle section'
CIRCULAR 1 RADIUS 10.0
END GEOMETRY_LIST
BEGIN CELL_GEOMETRY_TYPES
IGEOTYPE
CONSTANT 1
END CELL_GEOMETRY_TYPES
Define geometry for each section
Allocate Sections to all LNF cells
Define Options

## Slide 18
LNF Model: NPF Data
Read NPF data
Define Options
begin options
SAVE_FLOWS
HNOFLO -1E5 hnoflo
#VISCOSITY 1.0e-6
#GRAVITY 9.81
end options
#
begin npfdata
#
#icelltype(nodes) is 0:confined, 1:convertible
icelltype
constant 1
#
#ifdc(nodes) flow to dry cell correction option 0: no, 1: yes correct
ifdc
constant 0
#
#iflowtype(nodes) is the flag for flow equation for this cylinder
iflowtype
constant 4 Manning's equation
#
#chk(nodes) Manning's constant 0.013 s/m^1/3 converted to d/m^1/3
chk
constant 1.505e-7
end npfdata

## Slide 19
GWF1-LNF1 Exchange
Number of exchanges
List of exchange data
Define Options
begin options
PRINT_INPUT
PRINT_FLOWS
SAVE_FLOWS
NEWTON
# AUX testaux
end options
begin dimensions
NEXG 1
end dimensions
# GWnode LNFnode ifdc Icelltype Iflowtype FlenGW Kv Thick
begin exchangedata
#
20 1 0 1 3 50.0 1.0 1.0
end exchangedata
Similar file for GWF2-LNF1 Exchange

## Slide 20
Simulation Results
Head Distribution
Flux through Domain = 150 m3/day
Results compare with USG
Simulation Narrative
  Input readily constructed
  Outputs readily evaluated
  I think you will be quite excited to use the code or customize other processes/codes into it

## Slide 21: Questions
??
spanday@gsienv.com