## Slide 1: MODFLOW 6 LGR

## Slide 2: Local Grid Refinement
Why use LGR?
  Resolution can be increased in areas of interest
  Can be used with regular MODFLOW grids
  Child models can be extracted and run separately
Why not use it?
  More complicated to work with
  Concerns about accuracy
  Limited GUI support
  It used to be relatively slow and could have convergence problems

## Slide 3: Approaches
Old School (Telescopic Mesh Refinement)
  Heads or flows from a parent model are used to set boundary conditions for a child model
MODFLOW-LGR
  Parent and child models are iteratively coupled
MODFLOW-USG
  Parent and child models are built into a single mesh
MODFLOW 6
  Parent and child models are solved simultaneously in a single matrix solution

## Slide 4: 1. TMR
Heads and flows from parent model used as boundary conditions for child model
Easy to do
Some GUI support (e.g. Groundwater Vistas)
Child does not have to be coincident with parent
No automatic feedback from child to parent

## Slide 5: 2. MODFLOW-LGR
Parent and child models are iteratively coupled
Child models can be used separately
May be slow convergence
Limited GUI support
Restrictions on parent/child configurations

## Slide 6: 3. MODFLOW-USG
Parent, child, grandchildren, cousins, etc. are built into a single mesh
Some GUI support
Everything solved in a single matrix (fast and robust)
Need to reconstruct mesh to add a new child

## Slide 7: 4. MODFLOW 6
Can do single mesh or multiple models
Everything solved in a single matrix (fast and robust)
No GUI support yet

## Slide 8: MODFLOW 6 LGR
Construct parent and child models
Use IDOMAIN to inactivate parent model where child model exists
Use the GWF6-GWF6 Exchange (specified in mf6.nam) to couple the models

## Slide 9: Simulation Components
Timing Module
Solutions
Models
Exchanges
Utilities
Simulation
Solution 1
Model 4
Timing Module
Model 1
Model 3
Model 2
Exchange 1
Exchange 2
Exchange 3

## Slide 10: Multi-Model Simulation
MODFLOW 6 foundation allows models to be tightly coupled at the matrix level
Allows local grid refinement (LGR), and other model coupling strategies

## Slide 11: LGR Simulation
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2

## Slide 12: GWF Exchanges
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC

## Slide 13: LGR Simulation
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC
BEGIN OPTIONS
END OPTIONS
BEGIN TIMING
TDIS6 mysim.tdis
END TIMING
BEGIN MODELS
GWF6 parent.nam PARENT
GWF6 c1.nam C1
GWF6 c2.nam C2
GWF6 gc.nam GC
END MODELS
BEGIN EXCHANGES
GWF6-GWF6 parent-c1.exg PARENT C1
GWF6-GWF6 parent-c2.exg PARENT C2
GWF6-GWF6 c1-gc.exg C1 GC
END EXCHANGES
BEGIN SOLUTIONGROUP 1
IMS6 mysolver.ims PARENT C1 C2 GC
END SOLUTIONGROUP
Simulation Name File

## Slide 14: Matrix-Level Coupling
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC
Notes: Because our solver is unstructured and asymmetric, can handle Newton-Raphson, unstructured grids, ghost nodes, XT3D, dispersion tensors, etc…

## Slide 15: GWF6-GWF6 Exchange

## Slide 16: Map View
cl1
cl2
hwva
Cell in model 1
Cell in model 2
ihc = 1 or 2 (horizontal connection)

## Slide 17: Cross-Section View
TOP
BOT
ihc = 1
TOP
BOT
ihc = 2
“vertically staggered”

## Slide 18: Vertical Connections
hwva is the area of the connection
ihc = 0
cl1 is the half cell thickness of the cell in model 1
cl2 is the half cell thickness of the cell in model 2